Logbook of for the E&M experiment 2 (coils) for Group_7_Wednesday_20/03_13-15.
Students:
Martin Opat (s4704126)
Rick van Bruggen (s2491869)
TAs:
G. Katsanevakis
V. Atlasis

A.
- d in cm taken from center.
- start at 2cm from center, can’t go closer as probe not long enough and had to ensure stable distance r from - the line, so had to attach
- using rectangular probe
- current used = 1.95 A. distance probe from wire = 3cm
- zero out the gaussmeter holding null for 3sec
- earths field = 0.026mT, when 0 A ran through wire. Chosen to zero without black box so that we just measure the wire’s effect.
- sensitivty 10mT gaussmeter
- us moving slightly influences result by roughly 0.001 mT, so minimize moving
-length of half of wire used to measure, 15 cm.
- measured negative mT, but used positive as doesn’t change relation and if we move rod same thing
- markings on rod are 1 cm apart.
-improvement; higher amperage.

B.
- chosen to pick 4 cm from the center so that, field homogenoeus
- r = 2 cm so that the field is stronger as at 3cm distance, the B was 0 at start.
- for first run we picked 4 cm distance, then went minimally left and slight right for 2nd/3rd measurements.

C.
-rotate the wire 90deg for easier measuring. Check direction of B with right hand rule, put the rectangular probe facing upwards in the case we had, as B was going down when I directed towards us.
-white plastic part is d = 12 mm, diameter of wire = 6 mm. Decided to measure distance from the side of the wire, so nitial distance therefore is 3 mm.
- d is zero, as measuring at center.
-B earth is 0.0036 mT, but null again so not relevant for our data.
-pick higher current for more accurate data; 9.07 A.
-nulled so will measure until 0.0000 mT, not until lower than earth’s field

D. (parallel)
- R = 10.5 cm, of coils, so also 10.5 cm distance between them above each other. Measurements decided at height where height = 0 at bottom coil.
- use circular probe as it can hang from the top. Changed setup, see pic. Use ruler to align it to the center as well as possible. Error in placement is 1 cm as manual placing. Null again to avoid earth field
-coil does not hang exactly horizontally, but within range of error we start right at 0 cm above the coil, so center of coil. Height is height above the lower coil.
- amperage goes down slightly due to heating (?) resistance goes up when heat, so makes sense.
-ruler in the coils but shouldn’t have an effect.
-big error as coils are crooked.
-being in center exactly is irrelevant for the results as the point is to prove homogeneous field
-measured up to 14 cm which is 3.5cm above coil, then the B dropped >3pc so stopped.
-didn’t do below the bottom coil as the probe wasn’t long enough the way it was attached

E. (anti-parallel)
-Move cables to anti parallel.
-

F. (parallel)
-scale of newtonmeter = 0.2 N. error in reading off too, error in reading 0.005 N
-note that we wanna measure force in the center of configuration, but the force of the field pushes the meter up, so the field is less strong there, eventually it stabilizes; the magnet is slightly off center.
-data stays the same as gradient of B matters and B is consistent between two coils that run parallel, so no force exerted when the field changes.

F. (anti-parallel)
same as parallel.